## Slide 1: Autonomous Crop Row Detection for a Laser-based Weeding Robot
Roxane Mérat
Semester Project
Supervisors :
Cornelius von Einem
Patrick Barton
Prof. Dr. R. Siegwart

## Slide 2: The Caterra Project
Goal of Caterra :
Develop an autonomous agricultural robot with a laser module for weed removal
My goal :
Develop a robust crop rows detection algorithm using computer vision
Caterra’s agricultural robot

## Slide 3: State of the art
Excess green Index
Hough transform [1]
Deep Learning [2]
[1] : Real Time Tracking of Plant Rows Using a Hough Transform, John.A Marchant and Renaud Brivot
[2] : “From plants to landmarks: Time-invariant plant localization that uses deep pose regression in agricultural fields”, Kraemer et al.
Excess green index images
Hough Transform results

## Slide 4: Algorithm
 Use of temporal information : a crop should be in the same region in two sequential frames
Next Image
Image Pre-processing
Constrained Hough Transform
VP Calculation
Constrained RANSAC
Image
Is the error too big?
No
Yes

## Slide 5: Sky Removal
Calculate Laplacian
Original Image
Mask of the region with high Laplacian
Image with sky cut-off

## Slide 6: Vegetation Segmentation
main clustered colours
Original Image
Vegetation segmented
Canny Edges Detector
Advantages :
Threshold independent
Robust to shadows and colour variation

## Slide 7: Constrained Hough Transform
Vegetation Image
Image in Hough Space, the maximum value is taken
Line Detected
New masked image to be process
New Hough Space, band around detected angle

## Slide 8: Vanishing Point Calculation
Vanishing point = point described by main sinusoidal in Hough Space
Hough Transformation of a set of lines that intersect in a single point [1]
[1] : Vanishing Point Detection in the Hough Transform
Space, Andrea Matessi and Luca Lombardi

## Slide 9: Masking per crop
Each previously detected line is used to create the mask that will isolate the pixels corresponding to a single crop row in the next image
Mask
Vegetation Image
Crop Row masked
Lines found with Hough
Lines found with RANSAC

## Slide 10: RANSAC Lines
Detection with Hough Transform :
Every K frames
If distance between crop row too small
If angle too close to the horizon angle
If too few points for RANSAC

## Slide 11: Evaluation
Values [1] :
m – number of crop tbd
v0 – first line where evaluation starts
h – height of the image
u* – ground truth point on line v
u – my results of point on line v
d – distance between crops
σ – desired accuracy needed, 0.25 in my case
[1] : Method proposed by Vidovic et al., http://www.etfos.unios.hr/r3dvgroup/index.php?id=crd_dataset

## Slide 12: Results (1) :
Score = 0.92
Score = 0.98
Ground Truth
Results
Vegetation segmented
Original Image
Ground Truth
Results
Vegetation segmented
Original Image

## Slide 13: Results (2) :
Score = 0.93
Score = 0.85
On complete dataset : average score of 0.92 for non bushy images, 0.6 for bushy images
Ground Truth
Results
Vegetation segmented
Original Image
Ground Truth
Results
Vegetation segmented
Original Image

## Slide 14: Results (3)
Result of Caterra’s Dataset

## Slide 15: Failure Cases
Detection of curved crop rows
Very bushy crops

## Slide 16: Future Work
Optimize the code
Test it on different datasets : different soils and weather conditions
Calibration process

## Slide 17: Conclusion
Robust to different illuminations, points of view
Generalisable : not limited to one kind of plants
Accurate for straight crop row
Bushes can be a problem
Too slow, not yet able to work in real time

## Slide 18
Thank you !